## Slide 1: Govtech c01n BLE Remote
Reverse engineering Fujifilm’s BLE protocol
Jon Chiang

## Slide 2: # whoami
Cyber R&D engineer in CSIT
Worked at HP and Seagate as a firmware engineer
Freelance landscape & architectural photographer (IG: @jon.chiang)
Hobbyist electronics tinkerer

## Slide 3: About The Govtech c01n
A custom ESP32 microcontroller-based electronic CTF badge
Created by the founders of Alt-Tab Labs when they were in GovTech as interns
Electronic badge given out as prizes for GovTech’s Stack The Flags CTF competitions or as swag when you report a vulnerability
Uses the ESP32-WROVER-B microcontroller module with break outs, a d-pad and OLED screen
Intended to be GovTech Singapore’s version of an Arduino for electronic tinkering and hardware hacking
Built on MicroPython for ESP32
  Official Repo: https://github.com/c01nrepo/uPy_C01N_OS

## Slide 4: Since the badge has BLE…
And my Fujifilm GFX100s has BLE as well…why not make them talk to each other?
Both the C01N and the camera support Bluetooth 4.2 BLE
There’s an existing project (furble) that uses an ESP32 M5StickC as a Bluetooth remote: https://github.com/gkoh/furble
The C01N existing app store consists of only demo apps and games, so why not create something useful for myself?
To challenge myself to understand BLE and build a new app using C01N’s existing MicroPython codebase and libraries

## Slide 5: BLE Protocol Reverse Engineering
First, I need to understand how my camera pairs with my phone
Yeo Kheng Meng’s Intro to BLE series was instrumental in helping me with my understanding: https://engineers.sg/video/intro-to-bluetooth-low-energy-ble-hackware-v0-7--195
Quick Recap: Central vs Peripheral:
  Central: My phone or C01N, which will scan for BLE devices to connect to
  Peripheral: My Fujifilm GFX100s, which sends advertising packets and accepts connection requests from a central
Need to know how my camera introduces itself to the BLE world
GAP: Generic Access Profile, defines service discovery and connections to a central (handles Advertising)
GATT: Generic Attribute Profile, defines how data is exchanged upon connection (identifies Services, Characteristics and Descriptors)
Notes: Attribute Protocol (ATT): ATT is used to read, write, and exchange data between devices. It defines how data is organized and accessed in a BLE device, using attributes and services to represent device functionalities.
Generic Attribute Profile (GATT): GATT is built on top of the ATT protocol and defines a hierarchical data structure to organize data into services, characteristics, and descriptors. It specifies how data is exchanged between BLE devices.
Generic Access Profile (GAP): GAP defines the roles and modes of operation for BLE devices, such as peripheral, central, broadcaster, observer, etc. It also includes procedures for device discovery, connection establishment, and power management.

## Slide 6: BLE Protocol Reverse Engineering
Sniffing BLE traffic to obtain advertisement packets and observe BLE pairing protocol
I used an nRF52840 dongle for this (cheap, well documented and works with Wireshark)
Filter for the MAC address and Company ID of my camera
Got a bunch of packets:

## Slide 7: BLE Protocol Reverse Engineering
Breaking down Fujifilm’s advertising packets
Raw Advertising Data (30 bytes), consists of three main AD parts and is byte-order reversed (Little Endian):
Top part is nRF metadata
Each part always start with the length and type
Green: Length 0x02 and Type 0x01 (Flags)
Middle: Length 0x11 and Type 0x06 (ADV_TYPE_UUID128_MORE)
Orange: Length 0x08 and Type 0xFF (Manufacturer Specific Data)

## Slide 8: BLE Protocol Reverse Engineering
Breaking down the Manufacturer Specific Advertising Data portion (Type: 0xFF)
8 bytes long
Consists of 3 parts:
  Company ID: FUJIFILM Corporation (0x04D8)
  Fujifilm Type Token: 0x02
  “mToken” for pairing: last 4 bytes, generated randomly and must be used for pairing camera to a Central device

## Slide 9: Fujifilm’s BLE Pairing Procedure
Central (C01N) / GATT Client
Peripheral (Camera) / GATT Server
1. Scanning
2. Advertising packet received
3. Connection succeeded
4. Services discovered
5. Write mToken and C01N name to pairing characteristics
Advertising (publish mToken)
C01N connects, stop adverts
Send back pairing service info
Send back pairing characteristics info
Fuji broadcasts adv packets (GAP)
C01N connection attempt
Fuji services data (GATT)
Fuji characteristics data (GATT)
C01N discover pairing service
C01N discover pairing characteristics
6. Subscibe to Fuji’s notify and indication characteristics
7. Ready to use camera
Camera acknowledges write
C01N writes mToken and Name
Fuji write response
Send a configuration subscription response
C01N subscribes to characteristics
Subscription succeeded
Notes: Indication and notifications are commands that could be send through the attribute(ATT) protocol. So, there are two roles defined at the ATT layer:
Client devices access remote resources over a BLE link using the GATT protocol. Usually, the master is also the client but this is not required or mandatory.
Server devices have the GATT database, access control methods, and provide resources to the remote client. Usually, the slave is also the server.

## Slide 10: Implementing the pairing protocol
Critical services and characteristics for pairing
Pairing service and characteristics
Write mToken to _FUJIFILM_CHR_PAIR_UUID and
C01N’s name to _FUJIFILM_CHR_IDEN_UUID
Configuration service and characteristics
Subscribe to notification (NOT) and indication (IND) characteristics
Shutter and geotag (GPS) services
We write to these characteristics when we want to focus the lens or trigger the shutter, or record geolocation data
Notes: https://community.nxp.com/t5/Wireless-Connectivity-Knowledge/Indication-and-Notification/ta-p/1129270
Notification don't need acknowledged, so they are faster. Hence, server does not know if the message reach to the client.
Indication need acknowledged to communicated. The client sent a confirmation message back to the server, this way server knows that message reached the client

## Slide 11: Implementing the pairing protocol
MicroPython on the ESP32
The C01N was designed 5 years ago and uses an old release of the MicroPython core, which does not have BLE support
Downloaded the latest MicroPython firmware for the ESP32-WROVER-B over at https://micropython.org/download/ESP32_GENERIC/
Studied MicroPython’s Bluetooth API (https://docs.micropython.org/en/latest/library/bluetooth.html) – first iteration of my code did not have support for subscribing to a service to get indications and notifications
  Only could scan, connect and write to characteristics
Dug around the MicroPython Github and found the ‘aioble’ library, which is an asyncio-based wrapper for the Bluetooth API with the necessary classes and methods to support more BLE functionality
  Example code available to get myself started
  No need to reinvent the wheel to implement additional functionality
Also referred to furble’s implementation of the Fuji pairing protocol (saved me a ton of work!)

## Slide 12: Implementing the Shutter protocol
Firing the shutter release involves writing to the shutter characteristic (GATT Write)
Byte arrays for shutter action types
Must be written to the shutter characteristic using write-with-response, peripheral responds with an acknowledgement
Functions for shutter actions
Writes FUJIFILM_SHUTTER_CMD first before writing the requested shutter action

## Slide 13: Programming the ESP32
Pretty straightforward, you just need to install some Python and ESP32 dependencies and clone the official C01N repo to your machine or VM
Grab these dependencies:
python3
pip3
adafruit-ampy (through pip3)
esptool (through pip3)
Use the flash.sh script to flash your MicroPython filesystem to the ESP32:
Rapid prototyping can be done with ampy to expedite the testing of code without the need for reflashing (time consuming):

## Slide 14: Current Features
Integrated as an “app” in the C01N’s MicroPython filesystem
Ability to scan for and pair with Fujifilm cameras (tested so far on my GFX100s)
Saves existing pairing information
Supports single autofocus, continuous autofocus and shutter release
My Github Fork: https://github.com/goldencopy/uPy_C01N_OS
To work on:
Connect to saved peripheral without initiating a new pairing sequence
Timelapse mode

## Slide 15: Demo

## Slide 16: THANK YOU!